3-Part CSI MasterFormat Specification

SECTION 10 2600

WALL AND DOOR PROTECTION

- - GENERAL

## SECTION INCLUDES

### Corner Guard, Extruded Vinyl, 3/4 inch, 1-1/2 inch, 3 inch Wing Sizes

### Corner Guard, Extruded Vinyl, 3/4 inch, 1-1/2 inch, 3 inch Wing Sizes, Adhesive backed tape mount

### Corner Guard, Extruded Vinyl, 1-1/2 inch, 3 inch Wing Sizes, Pre-drilled screw mount

## SUBMITTALS

### Comply with requirements of Section 01 33 00 Submittals.

### Product data: Submit manufacturer’s product data.

### Shop drawing: Submit shop drawings showing components, dimensions, anchorage details.

### Samples: Submit for approval 12 inch (304.8mm) long sample for each model and color specified, including end caps and corner units.

### Test reports: Submit manufacturer’s test reports and certification indicating compliance with applicable ADA and building code requirements

  - QUALITY ASSURANCE

    - Comply with NFPA 101 for interior finish materials. Smoke developed less than 450 degrees F and flame spread of 25 or less in accordance with ASTM E84.

  - DELIVERY, STORAGE AND HANDLING

### Delivery: Deliver materials to site in manufacturer’s original, unopened containers and packaging with labels clearly indicating manufacturer and material.

### Storage: Store materials indoors in a clean, dry area protected from damage and in accordance with manufacturer’s instructions.

### Handling: Protect materials during handling and installation to prevent damage

- - PRODUCTS

2.01 	MANUFACTURER

Babcock-Davis

9300 73rd Ave North

Brooklyn Park, MN 55428

PH: 888.412.3726

www.BabcockDavis.com

2.02 	CORNER GUARD, Extruded Vinyl

- Nystrom model CGVE extruded corner guard adhered to substrate corner with glue. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Wing size:

      - 3/4 inch (19.1mm) Model CGVE75S

      - 1-1/2 inch (38.1mm) Model CGVE15S

      - 3 inch (76.2mm) Model CGVE3S

    - Corner angle type: 90 degree standard 1/8 inch radius

  - Profile: High impact vinyl acrylic nominal 0.08 inch (2.03mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish.

  - Adhesion: Manufacturer recommended contact or mastic adhesive.

  - Color: To be selected from manufacture’s standard colors.

2.03 	CORNER GUARD, Extruded Vinyl, Adhesive backed foam tape

- Nystrom model CGVE-T extruded corner guard adhered to substrate corner adhesive backed tape. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Wing size

      - 3/4 inch (19.1mm) Model CGVE75S-T

      - 1-1/2 inch (38.1mm) Model CGVE15S-T

      - 3 inch (76.2mm) Model CGVE3S-T

    - Corner angle type: 90 degree standard 1/8 inch radius

  - Profile: High impact vinyl acrylic nominal 0.08 inch (2.03mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish.

  - Adhesion: Manufacturer applied adhesive backed tape.

  - Color: To be selected from manufacture’s standard colors.

2.04 	CORNER GUARD, Extruded Vinyl

- Nystrom model CGVE extruded corner guard adhered to substrate corner with glue. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Wing size:

      - 1-1/2 inch (38.1mm) Model CGVE15S-D

      - 3 inch (76.2mm) Model CGVE3S-D

    - Corner angle type: 90 degree standard 1/8 inch radius

  - Profile: High impact vinyl acrylic nominal 0.08 inch (2.03mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish.

  - Adhesion: Pre-drilled countersunk holes for #6 by 1-1/2 inch (38mm) sheet metal screw

  - Color: To be selected from manufacture’s standard colors.

- - EXECUTION

3.01 EXAMINATION

- Verify by examination that wall surface is acceptable to receive the specified bumper guard. Notify the Architect in writing if wall surfaces are not acceptable. Do not begin installation until unacceptable conditions have been corrected.

3.02 INSTALLATION

A. Install corner guards to wall securely in accordance with manufacturer’s written instructions.

B. Install corner guards accurately in location, alignment, and elevation.

C. Provide horizontal steel stud back up in drywall stud cavity to accept fasteners.

END OF SECTION

Rev 12/17