3-Part CSI MasterFormat Specification

SECTION 10 2600

WALL AND DOOR PROTECTION

- - GENERAL

## SECTION INCLUDES

### 6 inch (152.4mm) Hand Rail, Vinyl with Accent

## SUBMITTALS

### Comply with requirements of Section 01 33 00 Submittals.

### Product data: Submit manufacturer’s product data.

### Shop drawing: Submit shop drawings showing components, dimensions, anchorage details.

### Samples: Submit for approval 12 inch (304.8mm) long sample for each model and color specified, including end caps and corner units.

### Test reports: Submit manufacturer’s test reports and certification indicating compliance with applicable ADA and building code requirements

  - QUALITY ASSURANCE

    - Comply with NFPA 101 for interior finish materials. Smoke developed less than 450 and flame spread of 25 or less in accordance with ASTM E84.

  - DELIVERY, STORAGE AND HANDLING

### Delivery: Deliver materials to site in manufacturer’s original, unopened containers and packaging with labels clearly indicating manufacturer and material.

### Storage: Store materials indoors in a clean, dry area protected from damage and in accordance with manufacturer’s instructions.

### Handling: Protect materials during handling and installation to prevent damage

- - PRODUCTS

2.01 	MANUFACTURER

Babcock-Davis

9300 73rd Ave N

Brooklyn Park, MN 55428

PH: 888.412.3726

www.BabcockDavis.com

2.02 	HAND RAIL, Vinyl, 6 inch with Accent and Vinyl Handgrip

- Babcock-Davis model BHRVE6C-AS hand rail is a three piece component consisting of a round vinyl handgrip, vinyl accent strip and 4 inch profile extrusion mounted over continuous aluminum retainer and mounting brackets maintaining wall clearance. Exposed surfaces shall be free of wrinkling, chipping, discoloration, or other imperfections.

  - Dimensions

    - Height: 6 inch (152.4mm)

    - Width of Grip: 1-1/2 inch (38.1mm)

    - Clearance from Wall: 1-11/16 inch (42.7mm) Bracket

  - Profile: High impact vinyl acrylic extrusion locked into place, nominal 0.078 inch (1.98mm) thick. Class A fire rating, tested in accordance with ASTM E 84.

  - Extrusion: Pebble grain finish in color selected from manufacture’s standard colors.

  - Retainer: Continuous 6063-T5 aluminum retainer along entire length of handrail bumper, nominal 0.060 inch (1.52mm) thick.

  - Accent Strip: Vinyl acrylic, color to be selected from manufacture’s standard colors.

  - Handgrip: 1-1/2 inch (38.1mm) diameter high impact acrylic in color selected from manufacture’s standard colors.

  - End Caps: Rigid plastic wall return unit of color and texture similar to that of rail.

  - Corners: External corner units of similar material to end cap units. Carry line of hand rail continuously around corner, unless otherwise indicated on drawings.

- - EXECUTION

3.01 EXAMINATION

- Verify by examination that wall surface is acceptable to receive the specified bumper guard. Notify the Architect in writing if wall surfaces are not acceptable. Do not begin installation until unacceptable conditions have been corrected.

3.02 INSTALLATION

A. Install hand rails to wall securely in accordance with manufacturer’s written instructions.

B. Install hand rails accurately in location, alignment, and elevation.

C. Provide horizontal steel stud back up in drywall stud cavity to accept fasteners.

END OF SECTION

Rev 12/17