MATrac  Roll Up Mat

Section: 12484 / 12 48 00

FLOOR GRATES AND FRAMES

- PART ONE - GENERAL

- SUMMARY

  - Section Includes

    - Floor Grids and Frame Assemblies

  - Related Sections

    - Section 03300 - Cast-In-Place Concrete: For concrete floor slab recess, and grouting frames into recess.

    - Section 07110 - Damp-proofing.

    - Section 15150 - Sanitary Waste and Vent Piping: For floor drain if applicable.

- REFERENCES

  - American Society for Testing and Materials (ASTM)

    - ASTM B 221-93 Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Shapes, and Tubes

  - American Architectural Manufacturers Association (AAMA)

    - AAMA 606.1 Voluntary Guide Specifications and Inspection Methods for Integral Color Anodic Finishes for Architectural Aluminum

    - AAMA 607.1 Voluntary Guide Specifications and Inspection Methods for Clear Anodic Finishes for Architectural Aluminum.

- SUBMITTALS

# Product Data: Manufacturers product specifications, installation and maintenance instructions.

# Shop Drawings: Show layout and types of grates and frames not less than half-scale sections of typical installations, details of patterns or designs, anchors, and accessories, and field measurements of slab recess to receive frames grates (if applicable).

# Samples for Selection Purposes: Actual sections of grate and frame material in a convenient but representative size showing full range of colors, textures, finishes and patterns available for each type of floor grate and frame specified.

# Samples for Verification Purposes: Not less than 6 inch square sections of grate material and 6 inch (152 mm) length of frame material in selected colors and finishes for each type of grate and frame specified.

# Installation, Operations and Maintenance data.

# QUALITY ASSURANCE

# Single Source Responsibility: Obtain floor grates and frames from one source and from a single manufacturer

# Rolling Load: 350 pounds per wheel.

# Uniform Load:  50,000 lbs per square foot

# SUBSTITUTIONS

# Proposals for substitution products shall be accepted only from bidding contractors and not less than (10) working days before bid due date. Contractor guarantees that proposed substitution shall meet the performance and quality standards of this specification.

# PROJECT CONDITIONS

# If product is to be recessed, coordinate with concrete work so that products are available for placing integrally with floor slabs.

# WARRANTY

# Floor mats and frames shall be fabricated free of defects in materials and workmanship in accordance with the General Conditions, and the manufacturer shall offer a 2 year warranty against defects in materials and workmanship.

- PART TWO - PRODUCTS

- ACCEPTABLE MANUFACTURERS

# Babcock-Davis

# 9300 73rd Avenue North

# Brooklyn Park, MN 55428

# PH: 888.412.3726

# FX: 888.312.3726

# Materials

# ENTRANCE SYSTEM FLOOR GRATE

  - Rail: Rigid PVC

  - Rail Finish: Rail finish shall be supplied in black (standard)

  - Rail Spacing: Spaced 1.875" (47.6MM) on center

  - Fasteners: Non-corrosive screws and anchors for securing frames together and to floors.

  - Construction:  Flexible low-density polyethylene hinge retained in a captive aluminum tread port. Tread cushions.

  - Rolling Load:  350-pounds per wheel.

  - Uniform Load:  300 lbs per square foot

# Tread Inserts

# NOTE TO SPECIFIER: You may select two treads; for example: Premium Carpet for absorbing and Vinyl for scraping.

# MATrac Roll up Mat with Premium carpet tread.  Tread insert:  Carpet fibers are 3700 denier solution-dyed woven nylon, and shall include a minimum of 100, 10 mil monofilament fibers per square inch. Available in one of 13 standard colors offered by manufacturer.  Each carpet fiber and monofilament shall be fusion-bonded to a rigid two-ply backing to prevent fraying and supplied in continuous spliced-free lengths.  Fibers shall be treated with anti-stain, anti-static and anti-microbial additives.  Carpet weight shall be 33 oz. /yd².

# MATrac Roll up Mat with RuggedScrub carpet tread: Crimped solution-dyed 600 denier polypropylene fibers tufted into a woven double backing and mechanically secured to tread rails. Available colors include: Charcoal, Chocolate Chip, Licorice, Tan, Navy or Black.

# 5 year warranty

# MATrac Roll up Mat with vinyl tread insert:  rubber convex profile and continuous serrations  Available colors include:   Blue, Grey, Beige, Red, Dark Brown, or Black.

# MATrac Roll up Mat with recycled rubber tread insert.  Tread insert: : ECO Surfaces® Recycled Rubber - High slip resistant rubber (SC of 90) insert manufactured with recycled rubber and EPDM (64%-92% dependent on color chosen).  Available colors include: Midnight Black, Blue Night, Rock Storm and Milky Way.

# MATrac Roll up Mat with TPV rubber tread insert: Rubber, with convex shape and continuous serrations.  Available Black Rubber color.

# MATrac Roll up Mat with vinyl abrasive tread: Vinyl abrasive factory bonded abrasive grit.  Available in Brick Red, Dark Brown, Ocean Grey, Safety Yellow, and Flat Black

# MATrac Roll up Mat with brush tread insert made with rigid nylon bristles, 9 tufts per inch, each tuft contains 80 bristles.  Available in black.

# ENTRANCE SYSTEM FLOOR GRATE FRAME (CALL FACTORY FOR CUSTOM COLORS).

# Aluminum Frame: ASTM B221, alloy 6063-T5

# Frame Finish: Finish shall be supplied in mill (standard) or one of 5 optional colors as offered by manufacturer.  (CALL FACTORY FOR CUSTOM COLORS).

# Mounting:

# SAM, Surface mounted, mechanically attached frame.  1 5/8” (41.3 mm) profile; 3/8” (9.5 mm) overall depth.   Frame finish shall be supplied in clear mill.

# SV, Surface mounted, Vinyl attached frame, shall have an overall depth of 3/8” (9.5mm) deep with a 1 5/8” (41.2mm) profile.  Frame finish shall be black.

# LBM, Level Bed, mechanically attached tapered angle frame, shall 7/16” (11.1 mm) deep with 1/8" (3.2mm) exposed surface.

# LBC, Level Bed, cast-in place frame, shall be 1 3/8” (34.9 mm) deep with 1/2" (12.7mm) exposed surface.

- PART 3 -  EXECUTION

- EXAMINATION

# Products must be placed on a flat and level substrate. Substrate shall meet tolerance of 1/8" (3.2mm) over 10 feet (3.28M) in accordance with ACI 302.

# Examine the substrates and conditions under which the work is to be performed, and notify the Contractor in writing of conditions detrimental to the proper and timely completion of the work. Do not proceed with the installation until unsatisfactory conditions have been corrected.

- INSTALLATION

# Install products in accordance with manufacturer’s instructions, at locations shown and with top of products level with adjoining finished flooring where applicable.

# Coordinate top of product surfaces with swinging doors to provide under-door clearance.

1. Provide necessary shims, spacers, and anchorages for proper location and secure attachment of frames to concrete.

2. For installation in terrazzo flooring, contact manufacturer.

- PROTECTION

# Upon completion of frame installations, provide temporary filler of plywood or fiberboard in grate recesses, and cover frames with plywood protective flooring. Maintain protection until construction traffic has ended and Project is near time of Substantial Completion.

# Install product when no further wheeled construction traffic will occur and wet type operations including painting and decorating are complete.